## Slide 1: How to: USB Terminal Server
Chris Kebriti and Sean Rendell
LabOps 2016

## Slide 2: Problem Statement
Many newer targets replaced the legacy RS232 console ports with USB console ports
There are no commercially available USB Terminal Servers (vs Digi PortServer) available to be configured for our needs (VLM integration)

## Slide 3: Requirements
Desktop Server (e.g. Dell Optiplex) running Linux (e.g. Ubuntu Server 14.04)
USB hub (e.g. 7-port)
USB -> RS232 Adapter (only for USB port discovery)
Network connection to Wind River
Optional: Arduino programmed to loop serial output

## Slide 4: Getting Started
Determining your USB Tree Topology
  Discovery
  Port Mapping (setting udev rules)
Test using Minicom (optional)
  Generate output to console for testing
Ser2net and VLM Integration

## Slide 5: Determining your USB Tree Topology
Problem:
  When a USB device is plugged in, the operating system maps it dynamically. By default, the OS does this in a very unpredictable way.
Goal:
  We want to achieve a deterministic fashion, e.g. port1=/dev/usb1, port2=/dev/usb2, etc. so that when we plug a device into the hub, we know exactly which name it was mounted under
Solution:
  Create persistent rules under /etc/udev/rules.d to identify and map to a consistent naming convention of our choice each time a device is plugged into the hub

## Slide 6: Determining your USB Tree Topology
We’re going to run a system program to monitor hotplug events
By running this while we hot-plug into each port, we can generate a log file which we can use to determine how each port is enumerated within the kernel

## Slide 7: Determining your USB Tree Topology
Let’s begin!
Plug the USB hub into any port on the Ubuntu server
Launch udevadm with the following command
    sudo udevadm monitor >& udev.log
    Note: this saves all stdout and err to a log. At the time of writing, I found that using “ | tee” did not work. I leave it to the reader to find a method of viewing the output while saving to a log.
Using a USB->Serial adapter, plug into each port of the hub in order (sequentially) allowing 8sec before removing
For more info on udevadm, see http://www.crashcourse.ca/wiki/index.php/Udev or refer to the man pages

## Slide 8: Determining your USB Tree Topology
Reviewing the output
Your log should look something like what’s shown on the right
We want to find a pattern so we can create a rule for mapping
Notice the pattern?
monitor will print the received events for:
UDEV - the event which udev sends out after rule processing
UDEV [206.699622] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4 (usb)
UDEV [206.700628] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0 (usb)
UDEV [206.700641] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0 (usb-serial)
UDEV [206.701527] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0/tty/ttyUSB0 (tty)
UDEV [211.814105] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0/tty/ttyUSB0 (tty)
UDEV [211.815760] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0 (usb-serial)
UDEV [211.815776] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0 (usb)
UDEV [211.815796] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4 (usb)
UDEV [216.475850] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3 (usb)
UDEV [216.476795] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3/1-3.3:1.0 (usb)
UDEV [216.477377] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3/1-3.3:1.0/ttyUSB0 (usb-serial)
UDEV [216.477970] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3/1-3.3:1.0/ttyUSB0/tty/ttyUSB0 (tty)
UDEV [221.081147] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3/1-3.3:1.0/ttyUSB0/tty/ttyUSB0 (tty)
UDEV [221.082795] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3/1-3.3:1.0/ttyUSB0 (usb-serial)
UDEV [221.082811] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3/1-3.3:1.0 (usb)
UDEV [221.082831] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.3 (usb)
UDEV [225.663725] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2 (usb)
UDEV [225.664831] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2/1-3.2:1.0 (usb)
UDEV [225.665548] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2/1-3.2:1.0/ttyUSB0 (usb-serial)
UDEV [225.665863] add /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2/1-3.2:1.0/ttyUSB0/tty/ttyUSB0 (tty)
UDEV [230.268995] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2/1-3.2:1.0/ttyUSB0/tty/ttyUSB0 (tty)
UDEV [230.270620] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2/1-3.2:1.0/ttyUSB0 (usb-serial)
UDEV [230.270636] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2/1-3.2:1.0 (usb)
UDEV [230.270656] remove /devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.2 (usb)

## Slide 9: Determining your USB Tree Topology
Take one these lines and try the following command:
$ udevadm info --attribute-walk --path=/devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0/tty/ttyUSB0
  looking at device '/devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0/tty/ttyUSB0': KERNEL=="ttyUSB0" SUBSYSTEM=="tty" DRIVER=="" looking at parent device '/devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0/ttyUSB0': KERNELS=="ttyUSB0" SUBSYSTEMS=="usb-serial" DRIVERS=="pl2303" ATTRS{port_number}=="0" looking at parent device '/devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4/1-3.4:1.0': KERNELS=="1-3.4:1.0" SUBSYSTEMS=="usb" DRIVERS=="pl2303" ATTRS{bInterfaceNumber}=="00" ATTRS{bAlternateSetting}==" 0" ATTRS{bNumEndpoints}=="03" ATTRS{bInterfaceClass}=="ff" ATTRS{bInterfaceSubClass}=="00" ATTRS{bInterfaceProtocol}=="00" ATTRS{supports_autosuspend}=="1" looking at parent device '/devices/pci0000:00/0000:00:1a.7/usb1/1-3/1-3.4': KERNELS=="1-3.4" SUBSYSTEMS=="usb"
For more info on udevadm info, try the man pages

## Slide 10: Determining your USB Tree Topology
Creating persistent rules for udev
Create a file under /etc/udev/rules.d/ named “60-perisitent-serial.rules”
  Note: ’60’ in the filename designates priority
Paste the text from the box below into the new file. Be sure to check the bold text matches your config
Notice the “=“ and the “==“
  ‘=‘ is the assignment
  ‘==‘ shows what information we are matching
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.4:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts1", SYMLINK="usb/ts_console1"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.3:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts2", SYMLINK="usb/ts_console2"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.2:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts3", SYMLINK="usb/ts_console3"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.4:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts4", SYMLINK="usb/ts_console4"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.3:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts5", SYMLINK="usb/ts_console5"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.2:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts6", SYMLINK="usb/ts_console6"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.1:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts7", SYMLINK="usb/ts_console7"
#Identifiable -> Assignment ->
Note: You must duplicate the table with different values for KERNEL. For instance, Arduino uses ‘ttyACM*’

## Slide 11: Determining your USB Tree Topology
Creating persistent rules for udev
#USB -> COM
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.4:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts1", SYMLINK="usb/ts_console1"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.3:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts2", SYMLINK="usb/ts_console2"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.2:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts3", SYMLINK="usb/ts_console3"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.4:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts4", SYMLINK="usb/ts_console4"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.3:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts5", SYMLINK="usb/ts_console5"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.2:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts6", SYMLINK="usb/ts_console6"
KERNEL=="ttyUSB*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.1:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts7", SYMLINK="usb/ts_console7"
#USB cable that connects to Arduino
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.4:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts1", SYMLINK="usb/ts_console1"
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.3:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts2", SYMLINK="usb/ts_console2"
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.2:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts3", SYMLINK="usb/ts_console3"
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.4:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts4", SYMLINK="usb/ts_console4"
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.3:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts5", SYMLINK="usb/ts_console5"
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.2:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts6", SYMLINK="usb/ts_console6"
KERNEL=="ttyACM*", SUBSYSTEMS=="usb", KERNELS=="1-3.1.1:1.0" GROUP="dialout", MODE="0666", NAME="ttyUSBts7", SYMLINK="usb/ts_console7“
...
Note: You must *duplicate* the table with different values for KERNEL. For instance, Arduino uses ‘ttyACM*’

## Slide 12: Determining your USB Tree Topology
In our assignments, we used a field called “SYMLINK”
Using this assignment, udev will now create a symbolic link under /dev/usb/ with the name given.
If you followed the instructions, you will now have your ports mapped consistently with the naming conventions
  USB hub port 1 = ts_console1
  USB hub port 2 = ts_console2
  …
Let test it!

## Slide 13: Determining your USB Tree Topology
Test that the rules we created are working correctly.
First, tell udev to read in the newly created rules
  $ sudo udevadm control --reload
Make a directory for the symlinks
  $ mkdir /dev/usb
Plug a device into hub that matches our newly created rules
Check for symlink
  $ ls -l /dev/usb

## Slide 14: Test using Minicom (optional)
Assumption: that you have some experience using an Arduino board and already own have installed the utility for programming on from your PC
The idea is to have known working test board to connect to with frequent intervals of console output
Once you have this, determine which USB port and run the following
  $ minicom -D /dev/usb/ts_console2 --baudrate 9600

## Slide 15: Ser2net and VLM Integration
ser2net provides a way for a user to connect from a network to a serial port [1]
It takes incoming TCP ports like telnet, and maps them to serial ports on the system
Install ser2net with the following command
  $ sudo apt-get install ser2net
Will be using some scripts developed internally, let’s go ahead and perform the following to prepare our system
  $ sudo apt-get install expect
  $ sudo apt-get remove resolvconf
For more information, use the man pages or visit the reference below
[1] http://ser2net.sourceforge.net/

## Slide 16: Ser2net and VLM Integration
Files | Changes
/etc/ser2net.conf | configure ser2net to use specific console ports with know port numbers and bauds
/etc/init.d/ser2net | change to allow admin console at port 2000
/home/username/digi_sim/digi_interface_sim.exp | creates the Digi interaction with an incoming VLM connection (or yourself if you want)
/home/username/digi_sim/start_digi_sim.sh | This starts a loop to keep the digi_interface_sim.exp running and sets up the fifos and nc
/home/username/digi_sim/fifo0 | created to allow bidirectional communication between the network and the digi_interface_sim.exp script
/home/username/digi_sim/fifo1 | created to allow bidirectional communication between the network and the digi_interface_sim.exp script
/home/username/digi_sim/README | notes
/etc/rc2.d/S90start_digi_sim | link that points to /etc/init.d/start_digi_sim.exp (to allow the service to start at boot time) ($ ln -s /etc/init.d/start_digi_sim.exp /etc/rc2.d/S90start_digi_sim)
/etc/init.d/start_digi_sim.sh | link that points start_digi_sim.sh ($ ln -s /home/username/digi_sim/start_digi_sim.sh /etc/init.d/start_digi_sim.sh) if the service ever stops, you can start this in the background to "restart" the service
/etc/udev/rules.d/60-persistent-serial.rules | Rules to map USB serial ports to a fixed name (completed first step of this BKM)
Files you will need to copy and modify
**Download files from HERE to your local machine and use WinSCP to copy to Linux machine**

## Slide 17: Ser2net and VLM Integration
In this file we are mapping the same physical USB ports to multiple network ports
This is to allow us to define 9600 and 115200 baud rates without having to restart ser2net
At a later step we will provision the terminal server in VLM to define 200 ports
2001:telnet:604800:/dev/usb/ts_console1:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2002:telnet:604800:/dev/usb/ts_console2:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2003:telnet:604800:/dev/usb/ts_console3:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2004:telnet:604800:/dev/usb/ts_console4:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2005:telnet:604800:/dev/usb/ts_console5:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2006:telnet:604800:/dev/usb/ts_console6:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2007:telnet:604800:/dev/usb/ts_console7:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2008:telnet:604800:/dev/usb/ts_console8:115200 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
# the same physical ports as above but at 9600 baud
2101:telnet:604800:/dev/usb/ts_console1:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2102:telnet:604800:/dev/usb/ts_console2:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2103:telnet:604800:/dev/usb/ts_console3:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2104:telnet:604800:/dev/usb/ts_console4:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2105:telnet:604800:/dev/usb/ts_console5:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2106:telnet:604800:/dev/usb/ts_console6:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2107:telnet:604800:/dev/usb/ts_console7:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
2108:telnet:604800:/dev/usb/ts_console8:9600 8DATABITS NONE 1STOPBIT -XONXOFF -RTSCTS LOCAL
/etc/ser2net.conf

## Slide 18: Ser2net and VLM Integration
VLM is coded to begin console sessions at port 2001
  E.g.
    Terminal Server Port # 1 = <ip-address>:2001 defined as baud rate 115200; USB port #1
    Terminal Server Port # 2 = <ip-address>:2002 defined as baud rate 115200; USB port #2
    Terminal Server Port # 3 = <ip-address>:2003 defined as baud rate 115200; USB port #3
    …
    Terminal Server Port # 101 = <ip-address>:2101 defined as baud rate 9600; USB port #1
    Terminal Server Port # 102 = <ip-address>:2102 defined as baud rate 9600; USB port #2
    …
/etc/ser2net.conf

## Slide 19: Ser2net and VLM Integration
Run /home/username/digi_sim/start_digi_sim.sh to start the service
You will only need to do this the first time
The file /etc/rc2.d/S90start_digi_sim will start the service every boot
  Note: the step above caused an issue after reboot due to Ubuntu’s method of encrypting (encrypt) the users directory and only mounting after login

## Slide 20: Ser2net and VLM Integration
In VLM, create a new Terminal Server and define it as 200 ports
  Choose a port in the 1-100 range for a baud rate of 115200
  Choose a port in the 101-200 range for a baud rate of 9600
  Note: this is all based off /etc/ser2net.conf
Take special care not to try and open the same offset port (e.g. 1 & 101). That is the same physical USB port. Nothing will prevent you from doing this!
VLM

## Slide 21: Thanks!